Linux kernel

---
Linux kernel key features
- Portability and hardware support
- Scalability
- Compliance to standards and interoperability
- Exhaustive networking support
- Stability and reliability
- Modularity
- Easy to program.

---
Linux kernel in the system
Application
…..
Application
…..
Library
Library
C Library
Linux Kernel
Hardware

---
Linux kernel

---
Linux kernel

---
Kernel Source
- https://www.kernel.org/
- Many chip vendors
- kernel sub-communities
  - Architecture communities
    - ARM, MIPS, PowerPC ...
  - device drivers communities
    - I2C, SPI, USB, PCI, network ...

---
Linux kernel size
- Linux 3.10 sources, Raw size: 573 MB
- Minimum Linux 3.17 compiled kernel size, booting on the ARM board
  - 876 KB (compressed)
  - 2.3 MB (raw)

---
Linux kernel size

---
Linux kernel size

---
Programming language
- Implemented in C like all Unix systems
- A little Assembly is used too
- No C++ used
- No C library
- No floating point computation
- Kernel code has to supply its own library implementations
  - X : printf(), memset(), malloc(),...
  - O: printk(), memset(), kmalloc()

---
Linux sources structure
- arch/<ARCH>
- Architecture specific code
  - arch/<ARCH>/mach-<machine>
  - arch/<ARCH>/include/asm
  - arch/<ARCH>/boot/
- driver/
- Documentation/

---
Kernel configuration
- The kernel configuration and build system is based on multiple Makefiles
- The configuration is stored in the .config file at the root of kernel sources
- As options have dependencies, typically never edited by hand, but through graphical or text interfaces
  - make menuconfig → Text
  - make xconfig → graphical

---
Kernel or module?
- The kernel image is a single file, resulting from the linking of all object files that correspond to features enabled in the configuration
- Some features (device drivers, filesystems, etc.) can however be compiled as modules

---
menuconfig

---
Kernel configuration options

---
Corresponding .config file excerpt

---
Kernel compilation
- Make
  - in the main kernel source directory
  - To run multiple jobs in parallel if you have multiple CPU cores
    - Make -j4
- Generates
  - arch/<arch>/boot/*Image
  - bzImage for x86, zImage for ARM, vmImage.gz for Blackfin

---
Make help

---
Module installation
- make modules_install
- Installs all modules in /lib/modules/<version>
- Module .ko (Kernel Object) files, in the same directory
  structure as in the sources.
- modules.alias
  - Module aliases for module loading utilities. Example line:
  - alias sound-service-?-0 snd_mixer_oss
- modules.dep
  - Module dependencies
- modules.symbols
  - Tells which module a given symbol belongs to

---
Kernel cleanup targets
- make clean
  - Kernel cleanup targets
- make mrproper
  - Remove all generated files (.config)
- make distclean
  - Remove editor backup and patch reject files

---
Specifying cross-compilation
- The CPU architecture and cross-compiler prefix are defined through the ARCH and CROSS_COMPILE variables in the top-level Makefile
- ARCH
  - ARCH=arm
- CROSS_COMPILE
  - arm-linux-

---
Specifying cross-compilation
- make ARCH=arm CROSS_COMPILE=arm-linux- …
- export ARCH=arm
  export CROSS_COMPILE=arm-linux
- Add above setting to script
  - source set_arm_toolchain.sh

---
Predefined configuration files
- Default configuration files available, per board or per-CPU family
  - They are stored in arch/<arch>/configs/, and are just minimal .config files
- make tiny4412_linux_defconfig
- To create your own default configuration file
  - make savedefconfig, to create a minimal configuration file
  - mv defconfig arch/<arch>/configs/myown_defconfig

---
Building and installing the kernel
- Run make
- make modules_install is used even in embedded development, as it installs many modules and description files
- make INSTALL_MOD_PATH=<dir>
- modules_install

---
Booting with U-Boot
- The typical boot process is therefore:
- Load zImage at address X in memory
- Start the kernel with bootm X in U-boot
- X = 0x?0008000
  - For example :
    - dnw C0008000
    - bootm c0008000

---
Kernel command line
- The kernel command line is a string that defines various arguments to the kernel
  - root= for the root filesystem
  - console= for the destination of kernel messages
  - Documentation/kernel-parameters.txt
- kernel command line
  - In U-Boot, the contents of the bootargs
  - Built into the kernel, using the CONFIG_CMDLINE option

---
Linux Kernel Booting
- CPU mode
  - All forms of interrupts must be disabled (IRQs and FIQs)
  - The CPU must be in SVC mode
- Caches, MMUs
  - The MMU must be off.
  - Instruction cache may be on or off.
  - Data cache must be off

---
Linux Kernel Booting
- Bootloader run kernel with parameters
  - R0 = 0,
  - r1 = machine type number
  - r2 = physical address of tagged list

---
Linux Kernel Booting
zImage
decompression
Load device
driver
arch/arm/boot/compressed/head.S
ARM-specific
kernel code
mount rootFS
arch/arm/kernel/head.S
arch/arm/kernel/head-common.S
Environment
initialize
Processor
independent
kernel code
init/main.c: start_kernel